## Slide 1
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
1 / 29
Mid-Sem B. Tech.
Presentation on
Crowd-Verified Road Hazard Detection and Hazard-Aware Navigation using On-Device Deep Learning
Presented by
[Member 1 Name]
[Member 2 Name]
[Member 3 Name]
[Member 4 Name]
Project Guide
[Guide Name]
Department of Computer Science & Engineering
COEP Technological University, Pune
October 2026

## Slide 2: Data Sheet
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
2 / 29
Member 1
Name: [Member 1 Name]
MIS: [MIS No.]
Degree: B.Tech ([Batch])
Branch: [Branch]
Division: [Division]
Department: Computer Science and Engineering, COEP Technological University, Pune
Member 2
Name: [Member 2 Name]
MIS: [MIS No.]
Degree: B.Tech ([Batch])
Branch: [Branch]
Division: [Division]
Department: Computer Science and Engineering, COEP Technological University, Pune
Member 3
Name: [Member 3 Name]
MIS: [MIS No.]
Degree: B.Tech ([Batch])
Branch: [Branch]
Division: [Division]
Department: Computer Science and Engineering, COEP Technological University, Pune
Member 4
Name: [Member 4 Name]
MIS: [MIS No.]
Degree: B.Tech ([Batch])
Branch: [Branch]
Division: [Division]
Department: Computer Science and Engineering, COEP Technological University, Pune

## Slide 3: Contents
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
3 / 29
1
Introduction
2
Literature Review
3
Problem Statement
4
Objectives
5
SRS
6
Proposed Methodology
7
Results & Discussion
8
Conclusion & Future Scope
9
Publication
10
References

## Slide 4: Introduction
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
4 / 29
Road hazards (accidents, fallen objects, floods, potholes) are usually discovered by a driver only on reaching them.
Navigation apps depend on drivers reporting hazards by hand, and on other drivers confirming or clearing them by hand [13].
Earlier crowdsensing used phone vibration and GPS, which only notices a hazard after driving over it [1, 2].
Compact detectors (YOLO family) now run on a phone in real time [8–12], so a dashcam phone can see hazards ahead.
BAGS: a dashcam phone detects hazards on-device, shares them, warns cars that are heading for them, reroutes drivers, and clears hazards automatically.
4.61 lakh
road accidents in India in 2022, claiming 1.68 lakh lives [21]
9.8 min
earlier than probe data: how much sooner crowd reports flag incidents [13]
Notes: Motivation: early, shared, automatic hazard information saves time and risk. The two numbers are cited: MoRTH 2022 report and the Waze reliability study.

## Slide 5: Literature Review
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
5 / 29
1. Sensor crowdsensing
Accelerometer + GPS on taxis or phones finds potholes and braking [1, 2]. Detects only after the car hits the hazard.
2. Vision road damage
Smartphone images + CNNs classify cracks and potholes; large public datasets [3, 4]. Offline surveys, no live alerts.
3. Dashcam accident models
Accident anticipation and anomaly detection in driving video [5–7]. Heavy models; protect only the ego car.
4. Efficient detectors
YOLO one-stage detection [8], NMS-free YOLOv10 [9], YOLO11 / YOLO26 [10, 11], int8 inference [12].
5. Crowd reports and trust
Waze reports are early but partial [13]; truth discovery weighs noisy sources [14]; V2X DENM shares events [17].
6. Routing on OSM
OSRM with contraction hierarchies [15, 16]; avoid-area routing via OpenRouteService [20].
Notes: Six strands of prior work. Each solves one piece; none closes the loop from detection to verified, automatically cleared alerts and rerouting.

## Slide 6: Literature Review: Comparison
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
6 / 29
System | Camera | On-device | Shares | Auto-confirm | Auto-clear | Direction | Reroute
Pothole Patrol [1] | ✗ | ~ | ~ | ✓ | ✗ | ✗ | ✗
Nericell [2] | ✗ | ✓ | ~ | ✗ | ✗ | ✗ | ✗
Maeda et al. [3] | ✓ | ✓ | ✗ | ✗ | ✗ | ✗ | ✗
Accident anticipation [5–7] | ✓ | ✗ | ✗ | ✗ | ✗ | ✗ | ✗
Waze reports [13] | ✗ | ~ | ✓ | ~ | ~ | ✗ | ✓
ETSI DENM (V2X) [17] | ✗ | ✓ | ✓ | ✗ | ~ | ✓ | ✗
BAGS (this work) | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
Table 1: Capabilities of prior systems (✓ yes, ~ partial or manual, ✗ no), from the cited descriptions
Prior work covers single steps; none verifies hazards from several cars and clears them automatically.
Manual platforms rely on drivers tapping "still there?"; BAGS uses passing cameras instead.

## Slide 7: Research Gap
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
7 / 29
Current limitations
Vision-based road studies stop at detection: results are not shared with the cars that are about to meet the hazard.
Crowd platforms trust one manual report and keep a hazard until someone manually clears it or a fixed timeout passes.
A single false detection can reroute every car, because no confirmation step is applied.
Hazards on the far carriageway of a divided road are treated as being on the driver's route.
Phones can only receive alerts while near the hazard; drivers heading for it from far away are not told in time to reroute.

## Slide 8: Problem Statement
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
8 / 29
Core problem: build a system in which phones detect road hazards on-device from a dashcam feed, and the hazards are verified by several cars, sent to the drivers they affect, routed around, and removed automatically once the road is clear.
Why it matters
Earlier warning for drivers approaching a blocked road, and fewer secondary collisions.
No manual reporting while driving, which is itself a distraction.
Stale hazards stop sending drivers on needless detours.
Only small JSON events leave the phone: no video upload, low data use.

## Slide 9: Objectives
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
9 / 29
Primary objectives
1
Run a YOLO hazard detector on the phone at ~3 frames/s and report detections with GPS position and direction of travel.
2
Merge repeat reports into hazards on a server, and confirm them only with two cars or one very confident detection.
3
Push each hazard to cars within 2 km or navigating a route that passes it ahead.
4
Plan hazard-aware routes and offer reroutes, and faster routes once a hazard clears.
5
Expire hazards by type and clear them when passing cars no longer see them.
6
Compare three detector generations for size, speed and accuracy.

## Slide 10: Existing Methodology
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
10 / 29
1
Manual crowd reporting
Waze-style: a driver taps a report; others confirm or clear it by hand [13]. Driver distraction; stale reports.
2
Sensor crowdsensing
Accelerometer/GPS anomalies aggregated on a server [1, 2]. Hazard found only after it is hit.
3
Offline vision surveys
Smartphone images labelled with CNN detectors for road-maintenance maps [3, 4]. No real-time sharing.
4
V2X event messages
ETSI DENM broadcasts events between equipped vehicles [17]. Needs special radios; no camera verification.

## Slide 11: SDLC Model and SRS
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
11 / 29
SDLC model: iterative and incremental prototyping. Detection, reporting, alerts, routing and hazard verification were built and tested on Android in stages, each followed by automated tests and a test drive.
Table 2: Software Requirements Specification (SRS)
Type | Requirement
Functional | Detect accident, fallen object and flood on-device from the camera at ~3 fps
Functional | Report type, confidence, GPS position and heading; merge repeats into one hazard
Functional | Push alerts to cars within 2 km or ahead on their route; show banner and map
Functional | Hazard-aware routing; reroute offer with 10 s countdown; faster route after clearance
Functional | Expire hazards by type; clear after 2 'not seen' votes from passing cars
Performance | Inference throttled to ≤ 3.3 fps; stale frames dropped, never queued
Privacy | No video leaves the phone; only small JSON events
Reliability | Network failures non-fatal; retried at next ping (20 s) or sync (15 s)
Environment | Android (Flutter 3.47.2), Python 3.13 + FastAPI + SQLite, Firebase FCM

## Slide 12: Functional Test Cases
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
12 / 29
Table 3: Functional test cases (all automated, all passing)
ID | Test input | Expected result
TC-01 | One car reports the same accident repeatedly while passing | One hazard; nearby cars pushed once
TC-02 | A second car reports the same hazard | Hazard confirmed; one more push
TC-03 | A single report with confidence 0.9 | Confirmed immediately
TC-04 | Two cars pass, detecting, without seeing it | Hazard deleted; apps drop it at next sync
TC-05 | 'Not seen' vote from a car going the other way | Vote ignored
TC-06 | Unconfirmed, or oncoming-only, accident on route | Warning only; no reroute
TC-07 | Detour around one hazard runs into another | Second avoid request includes both
TC-08 | 3 frames arrive while a detection waits for GPS | All 3 checked; one shared GPS lookup

## Slide 13: Proposed Methodology
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
13 / 29
Detect
YOLO on the phone checks ~3 frames/s; per-class thresholds
Report
Type, confidence, GPS and heading sent to the server
Verify
Repeats merged within 50 m; confirmed by 2 cars or confidence ≥ 0.8
Alert
FCM push to cars within 2 km, or ahead on their route
Reroute
Avoid confirmed hazards on this side of the road; 10 s offer
Clear
Expire by type; 2 passing cars that miss it remove it
Notes: The six-stage loop. Every stage after Detect is new relative to the vision papers in the review.

## Slide 14: Architectural Model
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
14 / 29
VEHICLE: BAGS APP (Flutter)
Navigation & map: hazard-aware routes, reroute offers
Dashcam camera (frames dropped to ~3 fps)
YOLO detector (TFLite, on-device)
Detection pipeline: per-class thresholds, GPS + heading
Clearance watcher: 'not seen' votes
Location pinger: position + route, every 20 s
ALERT SERVER (FastAPI + SQLite)
Merge sightings within 50 m
Confirm: 2 cars or conf ≥ 0.8
Expire per type; clear on 2 same-direction votes
Target pushes: ≤ 2 km, or ahead on route
GET /alerts (15 s sync)
EXTERNAL SERVICES
Routing & maps: OpenRouteService / OSRM, OSM
Firebase Cloud Messaging
route request (avoid areas)
detections
votes
pings
alerts
push
Other cars' phones: alert banner, map dot, reroute offer (and, when the road clears, a faster-route offer)
Figure 1: BAGS system architecture
Notes: Left: everything on the phone. Middle: the server keeps one record per hazard and decides who to tell. Right: Firebase delivers pushes; routing services plan routes.

## Slide 15: On-Device Detection Pipeline
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
15 / 29
Throttle: the camera gives ~30 frames/s; the model checks at most one per 300 ms. Frames arriving while it is busy are dropped, never queued.
Model-agnostic decoding: the app reads the output shape and handles a raw YOLO head (box + class scores, NMS in the app) or an end-to-end head (NMS inside the model).
Per-class thresholds: report the most confident box that passes its own class threshold (e.g. flood 0.25, accident 0.469).
Location and heading: one GPS lookup is shared by a burst of detections; the model keeps checking frames meanwhile. Heading is kept only above 2 m/s.
Reported detection = argmax over boxes b with conf(b) ≥ τ(class(b)) of conf(b)
τ: accident 0.469 · fallen object 0.477 · flood 0.25 · clear road 0.406
If no box passes, the most confident box is shown on screen but not reported.

## Slide 16: Hazard Lifecycle on the Server
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
16 / 29
Merge: a report of the same type within 50 m of a live hazard is a sighting of it, not a new hazard.
Confirm: a hazard reroutes cars only when reporters ≥ 2 or max confidence ≥ 0.8. Unconfirmed hazards still warn (faded on the map).
Clear: deleted once 2 different cars drive past, detecting, without seeing it, with no sighting since.
Table 4: Lifetime after the last sighting, by hazard type
Hazard type | Lifetime | Effect on routing
Accident | 1 hour | Reroute (when confirmed)
Fallen object | 1 hour | Reroute (when confirmed)
Flood | 6 hours | Reroute (when confirmed)
Pothole | 7 days | Warning only
Other / new label | 2 hours | Warning only

## Slide 17: Direction-Aware Hazard Relevance
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
17 / 29
Δθ(a, b) = | ((a − b + 180) mod 360) − 180 |
Same way ⇔ Δθ ≤ 60°, compared with the route's direction within ±30 m of the hazard
Each report carries the reporting car's heading; each hazard lists its reporters' headings.
Reroute: only for hazards reported going the same way as the route. Oncoming-only reports stay as warnings (an undivided road may still be blocked).
Push: cars far ahead on a route are told only about hazards reported in their direction.
Votes: a car going the other way cannot clear a hazard; its camera may have faced away.
Hazards with no known heading count for everyone, as before.

## Slide 18: Hazard-Aware Routing and Alerts
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
18 / 29
Route planning
With an OpenRouteService key: avoid 60 m circles around blocking hazards on the route's side, adding any the detour meets (up to 3 rounds).
Without: OSRM alternatives, then forced detours 400 m / 1 km beside the hazard.
Reroute offers
A confirmed hazard reported ahead shows a card: 'Keep route' or 'New route (10)', taken automatically after 10 s.
When a blocking hazard clears, a faster route is offered if it saves ≥ max(60 s, 5% of time left).
Who gets a push
Cars within 2 km of the hazard; plus confirmed hazards to navigating cars whose route (sent with each ping, thinned to 10 m) passes it ahead, within a 50 m corridor, if pinged in the last 2 min.
Keeping the map current
Hazards re-synced every 15 s along the trip; ones the server no longer lists disappear. Repeat sightings push only when a hazard is new or newly confirmed.

## Slide 19: Experimental Setup
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
19 / 29
Setup
Phone: Android (Redmi Note 8) mounted as a dashcam; app built with Flutter 3.47.2.
Server: FastAPI + SQLite on a laptop; pushes through the Firebase Admin SDK.
Models: YOLO11m, YOLO26n and YOLO11n trained by the team on 4 classes (accident, non-accident, fallen object, flood); ONNX converted to TFLite with onnx2tf.
Benchmark: Intel Core i7-1165G7, 640×640 input, batch 1, ONNX Runtime 1.26 CPU; mean of 20 runs after warm-up.
Verification: 46 Flutter and 21 Python automated tests, plus end-to-end HTTP tests on a throwaway database.

## Slide 20: Model Comparison
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
20 / 29
Table 5: Detector generations used in BAGS
Metric | YOLO11m (v1) | YOLO26n (v2) | YOLO11n (v3)
Parameters (counted) | 20.10 M | 2.42 M | 2.62 M
TFLite size | 80.5 MB | 9.8 MB | 10.6 MB
Output head | Raw [1, 8, 8400] | End-to-end [1, 300, 6] | Raw [1, 8, 8400]
NMS | In the app | Inside the model | In the app
CPU latency, measured | 963 ms | 96 ms | 116 ms
COCO mAP50-95, published [10, 11] | 51.5 | 40.9 | 39.5
GFLOPs, published [10, 11] | 68.0 | 5.4 | 6.5
TFLite vs ONNX, max score error | 1.4×10⁻⁷ | 4.1×10⁻⁷ | 2.5×10⁻⁷
Hazard test-set mAP50 | [ML team] | [ML team] | [ML team]
On-phone time per frame | [measure] | [measure] | [measure]
Notes: Measured rows are from our own benchmark on a laptop CPU. Published rows are Ultralytics' COCO figures for each architecture, not our hazard dataset. Fill the last two rows from the ML team's validation run and the app's on-screen timing.

## Slide 21: Model Comparison: Size and Speed
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
21 / 29
Chart: CPU inference time (ms, measured)
| YOLO11m (v1) | YOLO26n (v2) | YOLO11n (v3)
Latency (ms) | 962.7 | 95.9 | 116.2
Chart: TFLite model size (MB)
| YOLO11m (v1) | YOLO26n (v2) | YOLO11n (v3)
Size (MB) | 80.5 | 9.8 | 10.6
The nano models are ~8× smaller and ~8–10× faster than YOLO11m, which makes ~3 fps on a phone realistic.
YOLO26n removes NMS from the app; YOLO11n needs NMS on the phone. The final choice depends on hazard test-set accuracy.

## Slide 22: System Results
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
22 / 29
15 → 2
pushes per nearby car for one hazard (reporter passes it, ~15 reports)
3 / 3
frames checked while a detection waits for GPS (was 1 / 3)
2 h → 1 h
accident lifetime, or minutes once 2 passing cars miss it
67
automated tests passing: 46 app (Flutter), 21 server (Python)
TFLite conversions match their ONNX originals to within 10⁻⁶ on all three models.
End-to-end over HTTP: 3 reports → 1 hazard, confirmed by the 2nd car; opposite-direction vote ignored; 2 votes clear it.

## Slide 23: Results and Discussion
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
23 / 29
Discussion
Merging and confirmation cut alert spam and stop one false detection from rerouting everyone.
Automatic clearance replaces the fixed 2-hour timeout, so detours end soon after the road is cleared.
Direction awareness avoids rerouting drivers for crashes on the far carriageway.
Limitations: hazard-dataset accuracy and on-phone timing are still to be measured; CPU timings are from a laptop; thresholds (0.8, 60°, 2 votes) need tuning on real drives; the server runs on a laptop.

## Slide 24: Novelty and Contributions
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
24 / 29
1
Negative-evidence clearance
Passing cars' cameras vote a hazard away; no driver input needed.
2
Direction-aware relevance
Rerouting, far pushes and votes respect which side of the road reported it.
3
Confirmation gate
Reroute only for 2 reporters or confidence ≥ 0.8; unconfirmed hazards still warn.
4
Route-ahead alerts and offers
Drivers heading for a hazard are told early; reroute and faster-route offers with a countdown.
5
Model-agnostic pipeline
Swappable detectors (raw or end-to-end heads), compared across three generations.

## Slide 25: Conclusion and Future Scope
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
25 / 29
Conclusion
BAGS closes the loop from on-device detection to verified alerts, rerouting and automatic clearance.
Nano YOLO models make on-phone detection practical at ~3 fps.
Crowd verification and direction awareness make shared hazards trustworthy.
Future scope
Measure hazard-dataset accuracy and on-phone speed; int8 quantisation.
Confirm or clear hazards from traffic speed in location pings, without a camera.
Tune thresholds on real drives; host the server in the cloud with authentication.
Spread rerouted cars across several detours (load-aware rerouting).

## Slide 26: Publication
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
26 / 29
Paper in preparation
"Crowd-Verified Road Hazard Detection and Hazard-Aware Navigation using On-Device Deep Learning"
Target venue: [to be decided]

## Slide 27: References
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
27 / 29
[1] J. Eriksson et al., "The Pothole Patrol: Using a mobile sensor network for road surface monitoring," in Proc. ACM MobiSys, 2008, pp. 29–39.
[2] P. Mohan, V. N. Padmanabhan, R. Ramjee, "Nericell: Rich monitoring of road and traffic conditions using mobile smartphones," in Proc. ACM SenSys, 2008, pp. 323–336.
[3] H. Maeda et al., "Road damage detection and classification using deep neural networks with smartphone images," Computer-Aided Civil and Infrastructure Engineering, vol. 33, no. 12, pp. 1127–1141, 2018.
[4] D. Arya et al., "RDD2022: A multi-national image dataset for automatic road damage detection," Geoscience Data Journal, 2024.
[5] F.-H. Chan, Y.-T. Chen, Y. Xiang, M. Sun, "Anticipating accidents in dashcam videos," in Proc. ACCV, 2016, pp. 136–153.
[6] W. Bao, Q. Yu, Y. Kong, "Uncertainty-based traffic accident anticipation with spatio-temporal relational learning," in Proc. ACM Multimedia, 2020.
[7] Y. Yao et al., "DoTA: Unsupervised detection of traffic anomaly in driving videos," IEEE Trans. Pattern Analysis and Machine Intelligence, vol. 45, no. 1, 2023.
[8] J. Redmon, S. Divvala, R. Girshick, A. Farhadi, "You only look once: Unified, real-time object detection," in Proc. IEEE CVPR, 2016, pp. 779–788.
[9] A. Wang et al., "YOLOv10: Real-time end-to-end object detection," in Proc. NeurIPS, 2024.
[10] G. Jocher, J. Qiu, "Ultralytics YOLO11," 2024. [Online]. Available: docs.ultralytics.com/models/yolo11
[11] Ultralytics, "YOLO26," 2025. [Online]. Available: docs.ultralytics.com/models/yolo26

## Slide 28: References (contd.)
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
28 / 29
[12] B. Jacob et al., "Quantization and training of neural networks for efficient integer-arithmetic-only inference," in Proc. IEEE CVPR, 2018, pp. 2704–2713.
[13] M. Amin-Naseri et al., "Evaluating the reliability, coverage, and added value of crowdsourced traffic incident reports from Waze," Transportation Research Record, vol. 2672, no. 43, pp. 34–43, 2018.
[14] Y. Li et al., "A survey on truth discovery," ACM SIGKDD Explorations, vol. 17, no. 2, pp. 1–16, 2016.
[15] D. Luxen, C. Vetter, "Real-time routing with OpenStreetMap data," in Proc. ACM SIGSPATIAL GIS, 2011, pp. 513–516.
[16] R. Geisberger, P. Sanders, D. Schultes, D. Delling, "Contraction hierarchies: Faster and simpler hierarchical routing in road networks," in Proc. WEA, LNCS 5038, 2008, pp. 319–333.
[17] ETSI EN 302 637-3 V1.3.1, "Intelligent Transport Systems; Vehicular communications; Basic set of applications; Part 3: Decentralized Environmental Notification Basic Service," 2019.
[18] D. H. Douglas, T. K. Peucker, "Algorithms for the reduction of the number of points required to represent a digitized line or its caricature," Cartographica, vol. 10, no. 2, pp. 112–122, 1973.
[19] Google, "Firebase Cloud Messaging documentation." [Online]. Available: firebase.google.com/docs/cloud-messaging
[20] HeiGIT, "openrouteservice API documentation." [Online]. Available: openrouteservice.org
[21] Ministry of Road Transport and Highways, Govt. of India, "Road Accidents in India 2022," 2023.

## Slide 29
Outline
Introduction
Literature Review
Problem Statement
Objectives
SRS
Proposed Methodology
Results & Discussion
Conclusion & Future Scope
Publication
References
29 / 29
Questions / Discussion